New Cost Analysis – 04.06.2020

Assumptions:
- no overhead for if statement testing which type of particle we have
- counting power by 2 as two mults
- each particle has approximately M = 13 neighbors
- counting minus variable ( - var) as a substraction

Base version (master branch)
Without considering SearchNeighbors, the cost of our code is:
C(N, Ni, Nb)	= (fladds/subs, flmults, fldiv, flsin/cos(N, Ni, Nb))
= (27N + 200Ni + 4Nb, 27N + 264Ni + 8Nb, 14N + 52Ni + 5Nb, 2Nb)
= 68N + 516Ni + 19Nb

Cost Analysis for SearchNeighbors:
In the base version, SearchNeighbors uses the functions AddNeighbor and KernelAndGradient. AddNeighbor doesn’t have any flops, KernelAndGradient instead has flops. In order to count them there must be done a distinction between the calls of KernelAndGradient:
1. i == j: KernelAndGradient performs 12 flops
2. i != j and neighbor2 == NULL: KernelAndGradient performs 25 flops
3. i != j and neighbor2 != NULL: KernelAndGradient performs 27 flops
Now looking at SearchNeighbors:
Total number of flops for SearchNeighbors:
- every particle has itself as neighbor → 14N flops
- every particle has other 12 neighbors for which KernelAndGradient is computed but KernelAndGradient is computed only once for every pair of neighbors →12 * 26N flops / 2 = 156N flops
- for every interior particle we compute the distance between the considered particle and the other interior particles with index higher than the index of the considered particle → 6sum from {k=1} to {N_i} {N_i - k} = 3Ni(Ni – 1) flops
- for every interior particle we compute the distance between the considered particle and every boundary particle → Ni * 6Nb flops
- for every repulsive particle we compute the distance between the considered particle and every ghost particle → Nr * 6Ng = (Nb/3) * 6(2Nb/3) = 4Nb²/3
So, the cost of SearchNeighbors is 14N + 156N + 3Ni² – 3Ni + 6Ni * Nb + 4Nb²/3.
The overall cost of the base version is:
C(N, Ni, Nb) = 68N + 516Ni + 19Nb + 14N + 156N + 3Ni² – 3Ni + 6Ni * Nb + 4Nb²/3
 = 238N + 513Ni + 19Nb + 3Ni² + 6Ni*Nb + 4Nb²/3

Optimization1 (optimization1 branch)
With this optimization, we introduced different kind of “KernelAndGradient”:
1. KernelAndGradient_zero: 0 flops
2. KernelAndGradient_unidirectional: 16 flops
3. KernelAndGradient_bidirectional: 18 flops
So, looking at SearchNeighbors:
Total number of flops for SearchNeighbors:
- every particle has itself as neighbor → 0 flops
- every particle has other 12 neighbors for which “KernelAndGradient” is computed but it is computed only once for every pair of neighbors →12 * 17N flops / 2 = 102N flops
- for every interior particle we compute the distance between the considered particle and the other interior particles with index higher than the index of the considered particle → 6sum from {k=1} to {N_i} {N_i - k} = 3Ni(Ni – 1) flops
- for every interior particle we compute the distance between the considered particle and every boundary particle → Ni * 6Nb flops
- for every repulsive particle we compute the distance between the considered particle and every ghost particle → Nr * 6Ng = (Nb/3) * 6(2Nb/3) = 4Nb²/3
So, the cost of SearchNeighbors is 102N + 3Ni² – 3Ni + 6Ni * Nb + 4Nb²/3.
The overall cost of optimization1 is:
C(N, Ni, Nb) = 68N + 516Ni + 19Nb + 102N + 3Ni² – 3Ni + 6Ni * Nb + 4Nb²/3
 = 170N + 513Ni + 19Nb + 3Ni² + 6Ni*Nb + 4Nb²/3

Optimization2 (optimization2_unrolling_factor_4 branch)
The number of flops shouldn’t change with respect to optimization1.
C(N, Ni, Nb) = 170N + 513Ni + 19Nb + 3Ni² + 6Ni*Nb + 4Nb²/3

Optimization3 (optimization3_vectorization branch)
The number of flops shouldn’t change with respect to optimization1 and optimization2.
C(N, Ni, Nb) = 170N + 513Ni + 19Nb + 3Ni² + 6Ni*Nb + 4Nb²/3

Optimization4 (optimization4 branch)
Instead of computing for every pair of particles the sqrt, it is computed only when needed in “KernelAndGradient”:
1. KernelAndGradient_zero: 0 flops
2. KernelAndGradient_unidirectional: 17 flops
3. KernelAndGradient_bidirectional: 19 flops
Total number of flops for SearchNeighbors:
- every particle has itself as neighbor → 0 flops
- every particle has other 12 neighbors for which “KernelAndGradient” is computed but it is computed only once for every pair of neighbors →12 * 18N flops / 2 = 108N flops
- for every interior particle we compute the distance squared between the considered particle and the other interior particles with index higher than the index of the considered particle → 5sum from {k=1} to {N_i} {N_i - k} = (5/2)Ni(Ni – 1) flops
- for every interior particle we compute the distance between the considered particle and every boundary particle → Ni * 5Nb flops
- for every repulsive particle we compute the distance between the considered particle and every ghost particle → Nr * 5Ng = (Nb/3) * 5(2Nb/3) = 10Nb²/9
So, the cost of SearchNeighbors is 108N + (5/2)Ni² – (5/2)Ni + 5Ni * Nb + 10Nb²/9.
The overall cost of optimization4 is:
C(N, Ni, Nb) = 68N + 516Ni + 19Nb + 108N + (5/2)Ni² – (5/2)Ni + 5Ni * Nb + 10Nb²/9
 = 176N + (1027/2)Ni + 19Nb + (5/2)Ni² + 5Ni*Nb + 10Nb²/9

Comparison between the number of flops for different versions of our code
~400 particles → Ni = 396, Nb = 497, N = 893
Version	Flops	% wrt base version
Base	~2405790	-
Optimization 1, 2, 3	~2345066	97.48%
Optimization 4	~2020511	83.99%

~4000 particles → Ni = 3959, Nb = 1529, N = 5488
Version	Flops	% wrt base version
Base	~89824192	-
Optimization 1, 2, 3	~89451008	99.59%
Optimization 4	~75076244	83.58%